Signal & Image Processing

conv( A, B )
conv( A, B, shape )
- 1D convolution of vectors A and B
- The orientation of the result vector is the same as the orientation of A (ie. either column or row vector)
- The shape argument is optional; it is one of:
"full"	=	return the full convolution (default setting), with the size equal to A.n_elem + B.n_elem - 1
"same"	=	return the central part of the convolution, with the same size as vector A

- The convolution operation is also equivalent to FIR filtering
- Examples:
  vec A(256, fill::randu);
  vec B(16, fill::randu);
  vec C = conv(A, B);
  vec D = conv(A, B, "same");
- See also:
  - conv2()
  - fft()
  - cor()
  - interp1()
  - Convolution in MathWorld
  - Convolution in Wikipedia
  - FIR filter in Wikipedia

conv2( A, B )
conv2( A, B, shape )
- 2D convolution of matrices A and B
- The shape argument is optional; it is one of:
"full"	=	return the full convolution (default setting), with the size equal to size(A) + size(B) - 1
"same"	=	return the central part of the convolution, with the same size as matrix A

- The implementation of 2D convolution in this version is preliminary
- Examples:
  mat A(256, 256, fill::randu);
  mat B(16, 16, fill::randu);
  mat C = conv2(A, B);
  mat D = conv2(A, B, "same");
- See also:
  - conv()
  - fft2()
  - interp2()
  - Convolution in MathWorld
  - Convolution in Wikipedia
  - Kernel (image processing) in Wikipedia

cx_mat Y =  fft( X )
cx_mat Y =  fft( X, n )
cx_mat Z = ifft( cx_mat Y )
cx_mat Z = ifft( cx_mat Y, n )
- fft(): fast Fourier transform of a vector or matrix (real or complex)
- ifft(): inverse fast Fourier transform of a vector or matrix (complex only)
- If given a matrix, the transform is done on each column vector of the matrix
- The optional n argument specifies the transform length:
  - if n is larger than the length of the input vector, a zero-padded version of the vector is used
  - if n is smaller than the length of the input vector, only the first n elements of the vector are used
- If n is not specified, the transform length is the same as the length of the input vector
- Caveat: the transform is fastest when the transform length is a power of 2, eg. 64, 128, 256, 512, 1024, ...
- By default, an internal FFT algorithm based on KISS FFT is used
- Since Armadillo 12.0, the FFTW3 library can be optionally used for faster execution, as follows:
  - ARMA_USE_FFTW3 must be defined before including the armadillo header:
    #define ARMA_USE_FFTW3
    #include <armadillo>
  - you will also need to link with the FFTW3 runtime library (eg. -lfftw3)
- Examples:
  vec X(100, fill::randu);
  cx_vec Y = fft(X, 128);
- See also:
  - fft2()
  - conv()
  - real()
  - fast Fourier transform in MathWorld
  - fast Fourier transform in Wikipedia

cx_mat Y =  fft2( X )
cx_mat Y =  fft2( X, n_rows, n_cols )
cx_mat Z = ifft2( cx_mat Y )
cx_mat Z = ifft2( cx_mat Y, n_rows, n_cols )
- fft2(): 2D fast Fourier transform of a matrix (real or complex)
- ifft2(): 2D inverse fast Fourier transform of a matrix (complex only)
- The optional arguments n_rows and n_cols specify the size of the transform; a truncated and/or zero-padded version of the input matrix is used
- Caveat: the transform is fastest when both n_rows and n_cols are a power of 2, eg. 64, 128, 256, 512, 1024, ...
- The implementation of the 2D transform in this version is preliminary
- Examples:
  mat A(100, 100, fill::randu);
  cx_mat B = fft2(A);
  cx_mat C = fft2(A, 128, 128);
- See also:
  - fft()
  - conv2()
  - real()
  - fast Fourier transform in MathWorld
  - fast Fourier transform in Wikipedia

interp1( X, Y, XI, YI )
interp1( X, Y, XI, YI, method )
interp1( X, Y, XI, YI, method, extrapolation_value )
- 1D data interpolation
- Given a 1D function specified in vectors X and Y (where X specifies locations and Y specifies the corresponding values),
  generate vector YI which contains interpolated values at locations XI
- The method argument is optional; it is one of:
"nearest"	=	interpolate using single nearest neighbour
"linear"	=	linear interpolation between two nearest neighbours (default setting)
"*nearest"	=	as per "nearest", but faster by assuming that X and XI are monotonically increasing
"*linear"	=	as per "linear", but faster by assuming that X and XI are monotonically increasing

- If a location in XI is outside the domain of X, the corresponding value in YI is set to extrapolation_value
- The extrapolation_value argument is optional; by default it is datum::nan (not-a-number)
- Examples:
  vec x = linspace<vec>(0, 3, 20);
  vec y = square(x);
  vec xx = linspace<vec>(0, 3, 100);
  vec yy;
  interp1(x, y, xx, yy); // use linear interpolation by default
  interp1(x, y, xx, yy, "*linear"); // faster than "linear"
  interp1(x, y, xx, yy, "nearest");
- See also:
  - interp2()
  - polyval()
  - linspace()
  - regspace()
  - conv()
  - interpolation in Wikipedia

interp2( X, Y, Z, XI, YI, ZI )
interp2( X, Y, Z, XI, YI, ZI, method )
interp2( X, Y, Z, XI, YI, ZI, method, extrapolation_value )
- 2D data interpolation
- Given a 2D function specified by matrix Z with coordinates given by vectors X and Y,
  generate matrix ZI which contains interpolated values at the coordinates given by vectors XI and YI
- The vector pairs (X, Y) and (XI, YI) define 2D coordinates in a grid;
  for example, X defines the horizontal coordinates and Y defines the corresponding vertical coordinates,
  so that ( X(m), Y(n) ) is the 2D coordinate of element Z(n,m)
- The length of vector X must be equal to the number of columns in matrix Z
- The length of vector Y must be equal to the number of rows in matrix Z
- Vectors X, Y, XI, YI must contain monotonically increasing values (eg. 0.1, 0.2, 0.3, ...)
- The method argument is optional; it is one of:
"nearest"	=	interpolate using nearest neighbours
"linear"	=	linear interpolation between nearest neighbours (default setting)

- If a coordinate in the 2D grid specified by (XI, YI) is outside the domain of the 2D grid specified by (X, Y),
  the corresponding value in ZI is set to extrapolation_value
- The extrapolation_value argument is optional; by default it is datum::nan (not-a-number)
- Examples:
  mat Z;
  Z.load("input_image.pgm", pgm_binary); // load an image in pgm format
  vec X = regspace(1, Z.n_cols); // X = horizontal spacing
  vec Y = regspace(1, Z.n_rows); // Y = vertical spacing
  vec XI = regspace(X.min(), 1.0/2.0, X.max()); // magnify by approx 2
  vec YI = regspace(Y.min(), 1.0/3.0, Y.max()); // magnify by approx 3
  mat ZI;
  interp2(X, Y, Z, XI, YI, ZI); // use linear interpolation by default
  ZI.save("output_image.pgm", pgm_binary);
- See also:
  - interp1()
  - regspace()
  - conv2()
  - reshape()
  - bilinear interpolation in Wikipedia

P = polyfit( X, Y, N )
polyfit( P, X, Y, N )
- Given a 1D function specified in vectors X and Y (where X holds independent values and Y holds the corresponding dependent values),
  model the function as a polynomial of order N and store the polynomial coefficients in column vector P
- The given function is modelled as:
  y = p0xN + p1xN-1 + p2xN-2 + ... + pN-1x1 + pN
  where pi is the i-th polynomial coefficient; the coefficients are selected to minimise the overall error of the fit (least squares)
- The column vector P has N+1 coefficients
- N must be smaller than the number of elements in X
- If the polynomial coefficients cannot be found:
  - P = polyfit( X, Y, N ) resets P and throws a std::runtime_error exception
  - polyfit( P, X, Y, N ) resets P and returns a bool set to false (exception is not thrown)
- Examples:
  vec x = linspace<vec>(0,4*datum::pi,100);
  vec y = cos(x);
  vec p = polyfit(x,y,10);
- See also:
  - polyval()
  - roots()
  - interp1()
  - polynomial in Wikipedia
  - least squares in Wikipedia
  - curve fitting in Wikipedia
  - least squares fitting in MathWorld

Y = polyval( P, X )
- Given vector P of polynomial coefficients and vector X containing the independent values of a 1D function,
  generate vector Y which contains the corresponding dependent values
- For each x value in vector X, the corresponding y value in vector Y is generated using:
  y = p0xN + p1xN-1 + p2xN-2 + ... + pN-1x1 + pN
  where pi is the i-th polynomial coefficient in vector P
- P must contain polynomial coefficients in descending powers (eg. generated by the polyfit() function)
- Examples:
  vec x1 = linspace<vec>(0,4*datum::pi,100);
  vec y1 = cos(x1);
  vec p1 = polyfit(x1,y1,10);
  vec y2 = polyval(p1,x1);
- See also:
  - polyfit()
  - roots()
  - interp1()
  - polynomial in Wikipedia