Statistics & Clustering

mean, median, stddev, var, range
mean( V ) mean( M ) mean( M, dim ) mean( Q ) mean( Q, dim )		⎫ ⎪ ⎬ mean (average value) ⎪ ⎭
median( V ) median( M ) median( M, dim )		⎫ ⎬ median ⎭
stddev( V ) stddev( V, norm_type ) stddev( M ) stddev( M, norm_type ) stddev( M, norm_type, dim )		⎫ ⎪ ⎬ standard deviation ⎪ ⎭
var( V ) var( V, norm_type ) var( M ) var( M, norm_type ) var( M, norm_type, dim )		⎫ ⎪ ⎬ variance ⎪ ⎭
range( V ) range( M ) range( M, dim )		⎫ ⎬ range (difference between max and min) ⎭

- For vector V, return the statistic calculated using all the elements of the vector
- For matrix M, find the statistic for each column (dim = 0), or each row (dim = 1)
- For cube Q, find the statistics of elements along dimension dim, where dim ∈ { 0, 1, 2 }
- The dim argument is optional; by default dim = 0 is used
- The norm_type argument is optional; by default norm_type = 0 is used
- For the var() and stddev() functions:
  - the default norm_type = 0 performs normalisation using N-1 (where N is the number of samples), providing the best unbiased estimator
  - using norm_type = 1 performs normalisation using N, which provides the second moment around the mean
- Caveat: to obtain statistics for an integer vector or matrix (eg. uvec, ivec), first use the conv_to() function to obtain a floating point representation (eg. vec)
- Examples:
  mat A(5, 5, fill::randu);
  mat B = mean(A);
  mat C = var(A);
  double m = mean(mean(A));
  vec v(5, fill::randu);
  double x = var(v);
  ivec w = {1, 2, 3, 4}; // integer vector
  double y = mean( conv_to<vec>::from(w) );
- See also:
  - cov()
  - cor()
  - hist()
  - histc()
  - quantile()
  - normpdf()
  - min() & max()
  - running_stat - class for running statistics of scalars
  - running_stat_vec - class for running statistics of vectors
  - gmm_diag / gmm_full - probabilistic clustering and likelihood calculation via Gaussian mixture models
  - kmeans()

cov( X, Y )
cov( X, Y, norm_type )
cov( X )
cov( X, norm_type )
- For two matrix arguments X and Y, if each row of X and Y is an observation and each column is a variable, the (i,j)-th entry of cov(X,Y) is the covariance between the i-th variable in X and the j-th variable in Y
- For vector arguments, the type of vector is ignored and each element in the vector is treated as an observation
- For matrices, X and Y must have the same dimensions
- For vectors, X and Y must have the same number of elements
- cov(X) is equivalent to cov(X, X)
- The norm_type argument is optional; by default norm_type = 0 is used
- the norm_type argument controls the type of normalisation used, with N denoting the number of observations:
  - for norm_type = 0, normalisation is done using N-1, providing the best unbiased estimation of the covariance matrix (if the observations are from a normal distribution)
  - for norm_type = 1, normalisation is done using N, which provides the second moment matrix of the observations about their mean
- Examples:
  mat X(4, 5, fill::randu);
  mat Y(4, 5, fill::randu);
  mat C = cov(X,Y);
  mat D = cov(X,Y, 1);
- See also:
  - cor()
  - statistics functions
  - running_stat_vec
  - Covariance in MathWorld

cor( X, Y )
cor( X, Y, norm_type )
cor( X )
cor( X, norm_type )
- For two matrix arguments X and Y, if each row of X and Y is an observation and each column is a variable, the (i,j)-th entry of cor(X,Y) is the correlation coefficient between the i-th variable in X and the j-th variable in Y
- For vector arguments, the type of vector is ignored and each element in the vector is treated as an observation
- For matrices, X and Y must have the same dimensions
- For vectors, X and Y must have the same number of elements
- cor(X) is equivalent to cor(X, X)
- The norm_type argument is optional; by default norm_type = 0 is used
- the norm_type argument controls the type of normalisation used, with N denoting the number of observations:
  - for norm_type = 0, normalisation is done using N-1
  - for norm_type = 1, normalisation is done using N
- Examples:
  mat X(4, 5, fill::randu);
  mat Y(4, 5, fill::randu);
  mat R = cor(X,Y);
  mat S = cor(X,Y, 1);
- See also:
  - cov()
  - conv()
  - statistics functions
  - running_stat_vec
  - Correlation in MathWorld
  - Autocorrelation in MathWorld

hist( V )
hist( V, n_bins )
hist( V, centers )
hist( X, centers )
hist( X, centers, dim )
- For vector V, produce an unsigned vector of the same orientation as V (ie. either uvec or urowvec) that represents a histogram of counts
- For matrix X, produce a umat matrix containing either column histogram counts (for dim = 0, default), or row histogram counts (for dim = 1)
- The bin centers can be automatically determined from the data, with the number of bins specified via n_bins (default is 10); the range of the bins is determined by the range of the data
- The bin centers can also be explicitly specified via the centers vector; the vector must contain monotonically increasing values (eg. 0.1, 0.2, 0.3, ...)
- Examples:
  vec v(1000, fill::randn); // Gaussian distribution
  uvec h1 = hist(v, 11);
  uvec h2 = hist(v, linspace<vec>(-2,2,11));
- See also:
  - histc()
  - quantile()
  - statistics functions
  - conv_to()

histc( V, edges )
histc( X, edges )
histc( X, edges, dim )
- For vector V, produce an unsigned vector of the same orientation as V (ie. either uvec or urowvec) that contains the counts of the number of values that fall between the elements in the edges vector
- For matrix X, produce a umat matrix containing either column histogram counts (for dim = 0, default), or row histogram counts (for dim = 1)
- The edges vector must contain monotonically increasing values (eg. 0.1, 0.2, 0.3, ...)
- Examples:
  vec v(1000, fill::randn); // Gaussian distribution
  uvec h = histc(v, linspace<vec>(-2,2,11));
- See also:
  - hist()
  - statistics functions
  - conv_to()

quantile( V, P )
quantile( X, P )
quantile( X, P, dim )
- For a dataset stored in vector V or matrix X, calculate the quantiles corresponding to the cumulative probability values in the given P vector
- For vector V, produce a vector with the same orientation as V and the same length as P
- For matrix X, produce a matrix with the quantiles for each column vector (dim = 0) or each row vector (dim = 1)
- The dim argument is optional; by default dim = 0
- The P vector must contain values in the [0,1] interval (eg. 0.00, 0.25, 0.50, 0.75, 1.00)
- The algorithm for calculating the quantiles is based on Definition 5 in:
  Rob J. Hyndman and Yanan Fan. Sample Quantiles in Statistical Packages. The American Statistician, 50(4), 361-365, 1996. DOI: 10.2307/2684934
- Examples:
  vec V(1000, fill::randn); // Gaussian distribution
  vec P = { 0.25, 0.50, 0.75 };
  vec Q = quantile(V, P);
- See also:
  - hist()
  - median()
  - normcdf()
  - quantile in Wikipedia

mat coeff = princomp( mat X )
cx_mat coeff = princomp( cx_mat X )
princomp( mat coeff, mat X )
princomp( cx_mat coeff, cx_mat X )
princomp( mat coeff, mat score, mat X )
princomp( cx_mat coeff, cx_mat score, cx_mat X )
princomp( mat coeff, mat score, vec latent, mat X )
princomp( cx_mat coeff, cx_mat score, vec latent, cx_mat X )
princomp( mat coeff, mat score, vec latent, vec tsquared, mat X )
princomp( cx_mat coeff, cx_mat score, vec latent, cx_vec tsquared, cx_mat X )
- Principal component analysis of matrix X
- Each row of X is an observation and each column is a variable
- output objects:
  - coeff: principal component coefficients
  - score: projected data
  - latent: eigenvalues of the covariance matrix of X
  - tsquared: Hotteling's statistic for each sample
- The computation is based on singular value decomposition
- If the decomposition fails:
  - coeff = princomp(X) resets coeff and throws a std::runtime_error exception
  - remaining forms of princomp() reset all output matrices and return a bool set to false (exception is not thrown)
- Examples:
  mat A(5, 4, fill::randu);
  mat coeff;
  mat score;
  vec latent;
  vec tsquared;
  princomp(coeff, score, latent, tsquared, A);
- See also:
  - eig_sym()
  - svd()
  - svd_econ()
  - principal components analysis in Wikipedia

normpdf( X )
normpdf( X, M, S )
For each scalar x in X, compute its probability density function according to a Gaussian (normal) distribution using the corresponding mean value m in M and the corresponding standard deviation value s in S:
	1		⎧		(x-m)2	⎫
y =	‒‒‒‒	exp	⎪	−0.5	‒‒‒‒‒‒	⎪
	s·√τ		⎩		s2	⎭

- X can be a scalar, vector, or matrix
- M and S can jointly be either scalars, vectors, or matrices
- If M and S are omitted, their values are assumed to be 0 and 1, respectively
- Caveat: to reduce the incidence of numerical underflows, consider using log_normpdf()
- Examples:
  vec X(10, fill::randu);
  vec M(10, fill::randu);
  vec S(10, fill::randu);
  vec P1 = normpdf(X);
  vec P2 = normpdf(X, M, S );
  vec P3 = normpdf(1.23, M, S );
  vec P4 = normpdf(X, 4.56, 7.89);
  double P5 = normpdf(1.23, 4.56, 7.89);
- See also:
  - log_normpdf()
  - normcdf()
  - randn()
  - gmm_diag / gmm_full - probabilistic clustering and likelihood calculation via Gaussian mixture models
  - normal distribution in Wikipedia

log_normpdf( X )
log_normpdf( X, M, S )
For each scalar x in X, compute the logarithm version of probability density function according to a Gaussian (normal) distribution using the corresponding mean value m in M and the corresponding standard deviation value s in S:
		⎧	1		⎧		(x-m)2	⎫	⎫
y =	log	⎪	‒‒‒‒	exp	⎪	−0.5	‒‒‒‒‒‒	⎪	⎪
		⎩	s·√τ		⎩		s2	⎭	⎭

			⎧		(x-m)2	⎫
=	−log(s·√τ)	+	⎪	−0.5	‒‒‒‒‒‒	⎪
			⎩		s2	⎭

- X can be a scalar, vector, or matrix
- M and S can jointly be either scalars, vectors, or matrices
- If M and S are omitted, their values are assumed to be 0 and 1, respectively
- Examples:
  vec X(10, fill::randu);
  vec M(10, fill::randu);
  vec S(10, fill::randu);
  vec P1 = log_normpdf(X);
  vec P2 = log_normpdf(X, M, S );
  vec P3 = log_normpdf(1.23, M, S );
  vec P4 = log_normpdf(X, 4.56, 7.89);
  double P5 = log_normpdf(1.23, 4.56, 7.89);
- See also:
  - normpdf()
  - gmm_diag / gmm_full - probabilistic clustering and likelihood calculation via Gaussian mixture models
  - normal distribution in Wikipedia

normcdf( X )
normcdf( X, M, S )
- For each scalar x in X, compute its cumulative distribution function according to a Gaussian (normal) distribution using the corresponding mean value m in M and the corresponding standard deviation value s in S
- X can be a scalar, vector, or matrix
- M and S can jointly be either scalars, vectors, or matrices
- If M and S are omitted, their values are assumed to be 0 and 1, respectively
- Examples:
  vec X(10, fill::randu);
  vec M(10, fill::randu);
  vec S(10, fill::randu);
  vec P1 = normcdf(X);
  vec P2 = normcdf(X, M, S );
  vec P3 = normcdf(1.23, M, S );
  vec P4 = normcdf(X, 4.56, 7.89);
  double P5 = normcdf(1.23, 4.56, 7.89);
- See also:
  - normpdf()
  - quantile()
  - randn()
  - normal distribution in Wikipedia
  - cumulative distribution function in Wikipedia

X = mvnrnd( M, C )
X = mvnrnd( M, C, N )
mvnrnd( X, M, C )
mvnrnd( X, M, C, N )
- Generate a matrix with random column vectors from a multivariate Gaussian (normal) distribution with parameters M and C:
  - M is the mean; must be a column vector
  - C is the covariance matrix; must be symmetric positive semi-definite (preferably positive definite)
- N is the number of column vectors to generate; if N is omitted, it is assumed to be 1
- Caveat: repeated generation of one vector (or a small number of vectors) using the same M and C parameters can be inefficient;
  for repeated generation consider using the generate() function in the gmm_diag and gmm_full classes
- If generating the random vectors fails:
  - X = mvnrnd(M, C) and X = mvnrnd(M, C, N) reset X and throw a std::runtime_error exception
  - mvnrnd(X, M, C) and mvnrnd(X, M, C, N) reset X and return a bool set to false (exception is not thrown)
- Examples:
  vec M(5, fill::randu);
  mat B(5, 5, fill::randu);
  mat C = B.t() * B;
  mat X = mvnrnd(M, C, 100);
- See also:
  - randn()
  - chi2rnd()
  - wishrnd()
  - cov()
  - .is_sympd()
  - gmm_diag / gmm_full - probabilistic clustering and likelihood calculation via Gaussian mixture models
  - multivariate normal distribution in Wikipedia

chi2rnd( DF )
chi2rnd( DF_scalar )
chi2rnd( DF_scalar, n_elem )
chi2rnd( DF_scalar, n_rows, n_cols )
chi2rnd( DF_scalar, size(X) )
- Generate a random scalar, vector or matrix with elements sampled from a chi-squared distribution with the degrees of freedom specified by parameter DF or DF_scalar
- DF is a vector or matrix, while DF_scalar is a scalar
- Each value in DF and DF_scalar must be greater than zero
- For the chi2rnd(DF) form, the output vector/matrix has the same size and type as DF; each element in DF specifies a separate degree of freedom
- Usage:
  - vector_type v = chi2rnd( DF ), where the type of DF is a real vector_type
  - matrix_type X = chi2rnd( DF ), where the type of DF is a real matrix_type
  - scalar_type s = chi2rnd<scalar_type>( DF_scalar ), where scalar_type is either float or double
  - vector_type v = chi2rnd<vector_type>( DF_scalar, n_elem )
  - matrix_type X = chi2rnd<matrix_type>( DF_scalar, n_rows, n_cols )
  - matrix_type Y = chi2rnd<matrix_type>( DF_scalar, size(X) )
- Examples:
  mat X = chi2rnd(2, 5, 6);
  mat A = randi<mat>(5, 6, distr_param(1, 10));
  mat B = chi2rnd(A);
- See also:
  - randg()
  - randn()
  - mvnrnd()
  - wishrnd()
  - size()
  - chi-squared distribution in Wikipedia

W = wishrnd( S, df )
W = wishrnd( S, df, D )
wishrnd( W, S, df )
wishrnd( W, S, df, D )
- Generate a random matrix sampled from the Wishart distribution with parameters S and df:
  - S is a symmetric positive definite matrix (eg. a covariance matrix)
  - df is a scalar specifying the degrees of freedom; it can be a non-integer value
- D is an optional argument; it specifies the Cholesky decomposition of S; if D is provided, S is ignored;
  using D is more efficient if wishrnd() needs to be used many times for the same S matrix
- If generating the random matrix fails:
  - W = wishrnd(S, df) and W = wishrnd(S, df, D) reset W and throw a std::runtime_error exception
  - wishrnd(W, S, df) and wishrnd(W, S, df, D) reset W and return a bool set to false (exception is not thrown)
- Caveat: for the inverse (inverted) Wishart distribution, use iwishrnd()
- Examples:
  mat X(5, 5, fill::randu);
  mat S = X.t() * X;
  mat W = wishrnd(S, 6.7);
- See also:
  - iwishrnd()
  - chi2rnd()
  - mvnrnd()
  - chol()
  - cov()
  - randn()
  - .is_sympd()
  - Wishart distribution in Wikipedia

W = iwishrnd( T, df )
W = iwishrnd( T, df, Dinv )
iwishrnd( W, T, df )
iwishrnd( W, T, df, Dinv )
- Generate a random matrix sampled from the inverse Wishart distribution with parameters T and df:
  - T is a symmetric positive definite matrix
  - df is a scalar specifying the degrees of freedom; it can be a non-integer value
- Dinv is an optional argument; it specifies the Cholesky decomposition of the inverse of T; if Dinv is provided, T is ignored
  using Dinv is more efficient if iwishrnd() needs to be used many times for the same T matrix
- If generating the random matrix fails:
  - W = iwishrnd(T, df) and W = iwishrnd(T, df, Dinv) reset W and throw a std::runtime_error exception
  - iwishrnd(W, T, df) and iwishrnd(W, T, df, Dinv) reset W and return a bool set to false (exception is not thrown)
- Caveat: for the plain (non-inverse) Wishart distribution, use wishrnd()
- Examples:
  mat X(5, 5, fill::randu);
  mat T = X.t() * X;
  mat W = iwishrnd(T, 6.7);
- See also:
  - wishrnd()
  - chol()
  - inv_sympd()
  - .is_sympd()
  - inverse Wishart distribution in Wikipedia

running_stat<type>
- Class for running statistics (online statistics) of scalars (one dimensional process/signal)
- Useful if the storage of all samples (scalars) is impractical, or if the number of samples is not known in advance
- type is one of: float, double, cx_float, cx_double
- For an instance of running_stat named as X, the member functions are:
X(scalar)		update the statistics using the given scalar
X.min()		current minimum value
X.max()		current maximum value
X.range()		current range
X.mean()		current mean or average value
X.var() and X.var(norm_type)		current variance
X.stddev() and X.stddev(norm_type)		current standard deviation
X.reset()		reset all statistics and set the number of samples to zero
X.count()		current number of samples

- The norm_type argument is optional; by default norm_type = 0 is used
- For the .var() and .stddev() functions, the default norm_type = 0 performs normalisation using N-1 (where N is the number of samples so far), providing the best unbiased estimator; using norm_type = 1 causes normalisation to be done using N, which provides the second moment around the mean
- The return type of .count() depends on the underlying form of type: it is either float or double
- Examples:
  running_stat<double> stats;
  for(uword i=0; i<10000; ++i)
  {
  double sample = randn();
  stats(sample);
  }
  cout << "mean = " << stats.mean() << endl;
  cout << "var = " << stats.var() << endl;
  cout << "min = " << stats.min() << endl;
  cout << "max = " << stats.max() << endl;
- See also:
  - running_stat_vec (running statistics of vectors)
  - statistics functions
  - gmm_diag / gmm_full - probabilistic clustering via Gaussian mixture models

running_stat_vec<vec_type>
running_stat_vec<vec_type>(calc_cov)
- Class for running statistics (online statistics) of vectors (multi-dimensional process/signal)
- Useful if the storage of all samples (vectors) is impractical, or if the number of samples is not known in advance
- This class is similar to running_stat, with the difference that vectors are processed instead of scalars
- vec_type is the vector type of the samples; for example: vec, cx_vec, rowvec, ...
- For an instance of running_stat_vec named as X, the member functions are:
X(vector)		update the statistics using the given vector
X.min()		vector of current minimum values
X.max()		vector of current maximum values
X.range()		vector of current ranges
X.mean()		vector of current means
X.var() and X.var(norm_type)		vector of current variances
X.stddev() and X.stddev(norm_type)		vector of current standard deviations
X.cov() and X.cov(norm_type)		matrix of current covariances; valid if calc_cov=true during construction of running_stat_vec
X.reset()		reset all statistics and set the number of samples to zero
X.count()		current number of samples

- The calc_cov argument is optional; by default calc_cov=false, indicating that the covariance matrix will not be calculated; to enable the covariance matrix, use calc_cov=true during construction; for example: running_stat_vec<vec> X(true);
- The norm_type argument is optional; by default norm_type = 0 is used
- For the .var() and .stddev() functions, the default norm_type = 0 performs normalisation using N-1 (where N is the number of samples so far), providing the best unbiased estimator; using norm_type = 1 causes normalisation to be done using N, which provides the second moment around the mean
- The return type of .count() depends on the underlying form of vec_type: it is either float or double
- Examples:
  running_stat_vec<vec> stats;
  vec sample;
  for(uword i=0; i<10000; ++i)
  {
  sample = randu<vec>(5);
  stats(sample);
  }
  cout << "mean = " << endl << stats.mean() << endl;
  cout << "var = " << endl << stats.var() << endl;
  cout << "max = " << endl << stats.max() << endl;
  //
  //
  running_stat_vec<rowvec> more_stats(true);
  for(uword i=0; i<20; ++i)
  {
  sample = randu<rowvec>(3);
  sample(1) -= sample(0);
  sample(2) += sample(1);
  more_stats(sample);
  }
  cout << "covariance matrix = " << endl;
  cout << more_stats.cov() << endl;
  rowvec sd = more_stats.stddev();
  cout << "correlations = " << endl;
  cout << more_stats.cov() / (sd.t() * sd);
- See also:
  - running_stat (running statistics of scalars)
  - statistics functions
  - cov()
  - cor()
  - gmm_diag / gmm_full - probabilistic clustering via Gaussian mixture models

kmeans( means, data, k, seed_mode, n_iter, print_mode )
- Cluster given data into k disjoint sets
- The means parameter is the output matrix for storing the resulting centroids of the sets, with each centroid stored as a column vector
- The data parameter is the input data matrix, with each sample stored as a column vector
- The k parameter indicates the number of centroids; the number of samples in the data matrix should be much larger than k
- The seed_mode parameter specifies how the initial centroids are seeded; it is one of:
keep_existing		use the centroids specified in the means matrix as the starting point
static_subset		use a subset of the data vectors (repeatable)
random_subset		use a subset of the data vectors (random)
static_spread		use a maximally spread subset of data vectors (repeatable)
random_spread		use a maximally spread subset of data vectors (random start)

  Caveat: seeding the initial centroids with static_spread and random_spread can be much more time consuming than with static_subset and random_subset
- The n_iter parameter specifies the number of clustering iterations; this is data dependent, but about 10 is typically sufficient
- The print_mode parameter is either true or false, indicating whether progress is printed during clustering
- If the clustering fails, the means matrix is reset and a bool set to false is returned
- For faster execution on multi-core machines, enable OpenMP in your compiler (eg. -fopenmp in GCC and clang)
- Caveat: for probabilistic clustering, use the gmm_diag or gmm_full classes instead
- Examples:
  uword d = 5; // dimensionality
  uword N = 10000; // number of vectors
  mat data(d, N, fill::randu);
  mat means;
  bool status = kmeans(means, data, 2, random_subset, 10, true);
  if(status == false)
  {
  cout << "clustering failed" << endl;
  }
  means.print("means:");
- See also:
  - gmm_diag / gmm_full
  - statistics functions
  - running_stat_vec
  - k-means clustering in Wikipedia
  - k-means clustering in MathWorld
  - OpenMP in Wikipedia

gmm_diag
gmm_full
- Classes for multi-variate probabilistic clustering and likelihood calculation via Gaussian Mixture Models (GMMs)
- Distribution of data is modelled as:
		n_gaus-1
p(x)	=	∑	hg N( x | mg , Cg )
		g=0

where:
  - x is a column vector
  - n_gaus is the number of Gaussians; n_gaus ≥ 1
  - N( x | mg , Cg ) represents a Gaussian (normal) distribution
  - each Gaussian g has the following parameters:
    - hg is the heft (weight), with constraints hg ≥ 0 and ∑hg = 1
    - mg is the mean vector (centroid) with dimensionality n_dims
    - Cg is the covariance matrix (either diagonal or full)
- gmm_diag is tailored for diagonal covariance matrices
- gmm_full is tailored for full covariance matrices
- gmm_diag is considerably faster than gmm_full, at the cost of some reduction in modelling accuracy
- Both gmm_diag and gmm_full include tailored k-means and Expectation Maximisation algorithms for learning model parameters from training data
- For faster execution on multi-core machines, enable OpenMP in your compiler (eg. -fopenmp in GCC and clang)
- Implementation details are available in the following paper:
  Conrad Sanderson and Ryan Curtin.
  An Open Source C++ Implementation of Multi-Threaded Gaussian Mixture Models, k-Means and Expectation Maximisation.
  International Conference on Signal Processing and Communication Systems, 2017.
- For an instance of gmm_diag or gmm_full named as M, the member functions and variables are:
M.log_p(V)		return a scalar representing the log-likelihood of vector V (of type vec)
M.log_p(V, g)		return a scalar representing the log-likelihood of vector V (of type vec), according to Gaussian with index g

M.log_p(X)		return a row vector (of type rowvec) containing log-likelihoods of each column vector in matrix X (of type mat)
M.log_p(X, g)		return a row vector (of type rowvec) containing log-likelihoods of each column vector in matrix X (of type mat), according to Gaussian with index g

M.sum_log_p(X)		return a scalar representing the sum of log-likelihoods for all column vectors in matrix X (of type mat)
M.sum_log_p(X, g)		return a scalar representing the sum of log-likelihoods for all column vectors in matrix X (of type mat), according to Gaussian with index g

M.avg_log_p(X)		return a scalar representing the average log-likelihood of all column vectors in matrix X (of type mat)
M.avg_log_p(X, g)		return a scalar representing the average log-likelihood of all column vectors in matrix X (of type mat), according to Gaussian with index g

M.assign(V, dist_mode)		return the index of the closest mean (or Gaussian) to vector V (of type vec); parameter dist_mode is one of: / eucl_dist Euclidean distance (takes only means into account) / prob_dist probabilistic "distance", defined as the inverse likelihood (takes into account means, covariances and hefts)
M.assign(X, dist_mode)		return a row vector (of type urowvec) containing the indices of the closest means (or Gaussians) to each column vector in matrix X (of type mat); parameter dist_mode is either eucl_dist or prob_dist (as per the .assign() function above)

M.raw_hist(X, dist_mode)		return a row vector (of type urowvec) representing the raw histogram of counts; each entry is the number of counts corresponding to a Gaussian; each count is the number times the corresponding Gaussian was the closest to each column vector in matrix X; parameter dist_mode is either eucl_dist or prob_dist (as per the .assign() function above)
M.norm_hist(X, dist_mode)		similar to the .raw_hist() function above; return a row vector (of type rowvec) containing normalised counts; the vector sums to one; parameter dist_mode is either eucl_dist or prob_dist (as per the .assign() function above)

M.generate()		return a column vector (of type vec) representing a random sample generated according to the model's parameters
M.generate(N)		return a matrix (of type mat) containing N column vectors, with each vector representing a random sample generated according to the model's parameters

M.save(filename)		save the model to a file and return a bool indicating either success (true) or failure (false)
M.load(filename)		load the model from a file and return a bool indicating either success (true) or failure (false)

M.n_gaus()		return the number of means/Gaussians in the model
M.n_dims()		return the dimensionality of the means/Gaussians in the model

M.reset(n_dims, n_gaus)		set the model to have dimensionality n_dims, with n_gaus number of Gaussians; all the means are set to zero, all covariance matrix representations are equivalent to the identity matrix, and all the hefts (weights) are set to be uniform

M.hefts		read-only row vector (of type rowvec) containing the hefts (weights)
M.means		read-only matrix (of type mat) containing the means (centroids), stored as column vectors

M.dcovs [only in gmm_diag]		read-only matrix (of type mat) containing the representation of diagonal covariance matrices, with the set of diagonal covariances for each Gaussian stored as a column vector; applicable only to the gmm_diag class

M.fcovs [only in gmm_full]		read-only cube containing the full covariance matrices, with each covariance matrix stored as a slice within the cube; applicable only to the gmm_full class

M.set_hefts(V)		set the hefts (weights) of the model to be as specified in row vector V (of type rowvec); the number of hefts must match the existing model
M.set_means(X)		set the means to be as specified in matrix X (of type mat); the number of means and their dimensionality must match the existing model

M.set_dcovs(X) [only in gmm_diag]		set the diagonal covariances matrices to be as specified in matrix X (of type mat), with the set of diagonal covariances for each Gaussian stored as a column vector; the number of covariance matrices and their dimensionality must match the existing model; applicable only to the gmm_diag class

M.set_fcovs(X) [only in gmm_full]		set the full covariances matrices to be as specified in cube X, with each covariance matrix stored as a slice within the cube; the number of covariance matrices and their dimensionality must match the existing model; applicable only to the gmm_full class

M.set_params(means, covs, hefts)		set all the parameters at the same time; the type and layout of the parameters is as per the .set_hefts(), .set_means(), .set_dcovs() and .set_fcovs() functions above; the number of Gaussians and dimensionality can be different from the existing model

M.learn(data, n_gaus, dist_mode, seed_mode, km_iter, em_iter, var_floor, print_mode) learn the model parameters via multi-threaded k-means and/or EM algorithms; return a bool value, with true indicating success, and false indicating failure; the parameters have the following meanings:

data		matrix (of type mat) containing training samples; each sample is stored as a column vector

n_gaus		set the number of Gaussians to n_gaus; to help convergence, it is recommended that the given data matrix (above) contains at least 10 samples for each Gaussian

dist_mode		specifies the distance used during the seeding of initial means and k-means clustering: / eucl_dist Euclidean distance / maha_dist Mahalanobis distance, which uses a global diagonal covariance matrix estimated from the training samples; this is recommended for probabilistic applications

seed_mode		specifies how the initial means are seeded prior to running k-means and/or EM algorithms: / keep_existing keep the existing model (do not modify the means, covariances and hefts) / static_subset a subset of the training samples (repeatable) / random_subset a subset of the training samples (random) / static_spread a maximally spread subset of training samples (repeatable) / random_spread a maximally spread subset of training samples (random start) / caveat: seeding the initial means with static_spread and random_spread can be much more time consuming than with static_subset and random_subset

km_iter		the number of iterations of the k-means algorithm; this is data dependent, but typically 10 iterations are sufficient

em_iter		the number of iterations of the EM algorithm; this is data dependent, but typically 5 to 10 iterations are sufficient

var_floor		the variance floor (smallest allowed value) for the diagonal covariances; setting this to a small non-zero value can help with convergence and/or better quality parameter estimates

print_mode		either true or false; enable or disable printing of progress during the k-means and EM algorithms

- Examples:
  // create synthetic data with 2 Gaussians
  uword d = 5; // dimensionality
  uword N = 10000; // number of vectors
  mat data(d, N, fill::zeros);
  vec mean0 = linspace<vec>(1,d,d);
  vec mean1 = mean0 + 2;
  uword i = 0;
  while(i < N)
  {
  if(i < N) { data.col(i) = mean0 + randn<vec>(d); ++i; }
  if(i < N) { data.col(i) = mean0 + randn<vec>(d); ++i; }
  if(i < N) { data.col(i) = mean1 + randn<vec>(d); ++i; }
  }
  // model the data as a diagonal GMM with 2 Gaussians
  gmm_diag model;
  bool status = model.learn(data, 2, maha_dist, random_subset, 10, 5, 1e-10, true);
  if(status == false)
  {
  cout << "learning failed" << endl;
  }
  model.means.print("means:");
  double scalar_likelihood = model.log_p( data.col(0) );
  rowvec set_likelihood = model.log_p( data.cols(0,9) );
  double overall_likelihood = model.avg_log_p(data);
  uword gaus_id = model.assign( data.col(0), eucl_dist );
  urowvec gaus_ids = model.assign( data.cols(0,9), prob_dist );
  urowvec hist1 = model.raw_hist (data, prob_dist);
  rowvec hist2 = model.norm_hist(data, eucl_dist);
  model.save("my_model.gmm");
- See also:
  - normpdf()
  - mvnrnd()
  - statistics functions
  - running_stat_vec
  - kmeans()
  - covariance matrix in Wikipedia
  - covariance matrix in MathWorld
  - Mahalanobis distance in Wikipedia
  - multivariate normal distribution in Wikipedia
  - mixture model in Wikipedia
  - k-means clustering in Wikipedia
  - k-means clustering in MathWorld
  - Expectation-Maximisation algorithm in Wikipedia
  - maximum likelihood in MathWorld
  - OpenMP in Wikipedia